## Slide 1
UR12e
Robotic Workcell
MoveIt2 Integration &
Hardware-in-the-Loop Control
ROS2 Humble
Ubuntu 24.04
Docker
MoveIt2
System Components
🤖
UR12e Robot Arm
6-DOF collaborative arm
✋
Robotiq 2F-85
Adaptive gripper
📷
Intel RealSense ×2
Depth cameras, scene modelled
🏭
Complete Workcell
Desk, walls, full collision scene
⚡
Action Server Bridge
Novel gripper architecture
1 / 4

## Slide 2
Architecture & Control Modes
2 / 4
System Architecture
Application Layer
Motion Scripts • Pick & Place • Vision
MoveIt2 Planning
OMPL • Collision Check • IK/FK
Action Server Bridge
ros2_control • Trajectory Ctrl • Gripper
Hardware Layer
UR12e (RTDE) • Robotiq (URCap) • RealSense
✓ Zero modifications to Universal Robots packages
Four Control Modes
1
Pure Simulation
Robot: Fake UR12e Gripper: Fake Gripper
2
URSim + URCap
Robot: URSim Gripper: URCap Gripper
3
Hybrid Mode
Robot: Real UR12e Gripper: Action Server
4
Full Production
Robot: Real UR12e Gripper: Real Gripper
Same code runs in ALL four modes →

## Slide 3
Technical Deep-Dive
3 / 4
Action Server Bridge
Key innovation for hardware-agnostic gripper control
Motion Script
FollowJointTrajectory Action
Action Server Bridge ← KEY
URScript to UR Controller
Robotiq URCap → Gripper
MoveIt2 Configuration
Complete planning setup for 7-DOF system
Planning Groups
• ur_manipulator — 6-DOF arm (base_link → tool0)
• gripper — 2F-85 adaptive finger joint
Controllers Active
• joint_state_broadcaster (continuous)
• scaled_joint_trajectory_controller
• robotiq_gripper_controller (action server)
URDF Architecture
• Fake hardware for gripper in URDF
• Real control via external Action Server
• generate_ros2_control_tag=false (UR macro)
100%
UR Package Integrity
4
Control Modes
<5ms
RTDE Loop
7-DOF
Total Planning
v1.1.8
Current Release

## Slide 4
Highlights & Future Work
4 / 4
Key Achievements
Zero modifications to UR packages — fully upstream-compatible
Action Server Bridge — hardware-agnostic gripper control
Four progressive control modes in a single codebase
Complete workcell scene — full collision avoidance
ROS_DOMAIN_ID isolation — production-safe networking
Docker-containerised URSim — reproducible simulation
Roadmap
Next
Vision-Guided Grasping
YOLOv8 + RealSense D435 integration — colleague pipeline ready for integration
Soon
Force Control
Gripper force feedback for compliant manipulation of fragile objects
Later
Multi-Robot Coordination
ROS_DOMAIN_ID per robot — isolated, coordinated workcells
R&D
Advanced Planning
Dynamic replanning, trajectory optimisation, reinforcement learning
UR12e Workcell • v1.1.8_2f-85 • Branch: ur12e_2f-85_action_server • ROS2 Humble
Questions?