## Slide 1
UR12e Robotic Workcell
MoveIt2 Integration & Hardware-in-the-Loop Control
ROS2 Humble • Universal Robots UR12e • Robotiq 2F-85 Gripper

## Slide 2
System Overview
Complete Robotic Workcell
• UR12e 6-DOF Robot Arm
• Robotiq 2F-85 Adaptive Gripper
• Intel RealSense Depth Cameras (2x)
• Complete Scene Modeling
• Hardware-in-the-Loop Capable
Technical Specifications
ROS2 Humble
Ubuntu 24.04 LTS
MoveIt2 Motion Planning
Docker Containerized
URSim Integration
Action Server Architecture

## Slide 3
System Architecture
Application Layer
Motion Planning Scripts • Vision-Guided Grasping • Pick-and-Place Operations
Planning Layer
MoveIt2 Framework • OMPL Path Planning • Collision Detection
Control Layer
ros2_control Framework • Joint Trajectory Controller • Action Server Bridge
Hardware Layer
UR12e Robot (RTDE) • Robotiq Gripper (URCap) • RealSense Cameras

## Slide 4
MoveIt2 Integration
Motion Planning Features OMPL Planning Pipeline Multiple planners: RRT, PRM, EST Optimized path generation Collision Avoidance Complete scene modeling Real-time collision checking Safe trajectory execution Kinematics & Dynamics Forward/inverse kinematics Robot-specific calibration Velocity/acceleration limits
Planning Groups
ur_manipulator 6-DOF arm control gripper Adaptive gripper control
Active Controllers
• joint_state_broadcaster
• scaled_joint_trajectory_controller
• robotiq_gripper_controller

## Slide 5
Four Control Modes
Flexible Architecture Supporting Multiple Deployment Scenarios
Pure Simulation
Robot: Fake UR12e Gripper: Fake Gripper Development & Testing
URSim + URCap
Robot: URSim Robot Gripper: URCap Gripper Realistic Simulation
Hybrid Mode
Robot: Real UR12e Gripper: Action Server Hardware Validation
Full Production
Robot: Real UR12e Gripper: Real Gripper Deployment Ready
✓ Same Code Works in All Modes • Progressive Testing Workflow • Zero Code Changes

## Slide 6
Action Server Bridge Architecture
ROS2 Motion Script
FollowJointTrajectory Action
Action Server Bridge
URScript Commands
UR Controller + URCap
Physical Gripper
Benefits: Clean Separation • Testable Components • Hardware Agnostic • Production Ready

## Slide 7
Key Achievements
✓
Clean Integration
Zero modifications to Universal Robots packages
✓
Four Control Modes
Pure sim, URSim, hybrid, and full production
✓
Action Server
Novel gripper control architecture
✓
Network Isolation
ROS_DOMAIN_ID for multi-robot setups
✓
Docker Ready
Complete containerized simulation
✓
Production Tested
Validated with real UR12e hardware

## Slide 8
Technical Implementation
Core Components
Package Structure my_ur_description/ ├── urdf/ │ └── ur_system.xacro ├── config/ │ ├── ur_controllers.yaml │ └── moveit_config/ ├── launch/ │ └── my_robot.launch.py └── scripts/ ├── robotiq_ursim_bridge.py └── robotiq_real_gripper.py
Key Configuration Files
ur_system.xacro
Complete robot description with scene
ur_controllers.yaml
Real & fake hardware configurations
moveit_config/
Planning groups & kinematics
docker-compose.yaml
URSim containerization

## Slide 9
Development Workflow
1
Pure Simulation
• Fake hardware testing • Motion planning dev • MoveIt2 config
2
URSim + URCap
• Realistic simulation • Gripper URCap testing • Complete workflow
3
Hybrid Mode
• Real UR12e control • Action server validation • Hardware testing
4
Full Production
• Real gripper integration • Production validation • Deployment

## Slide 10
Results & Metrics
100%
UR Package Integrity
Zero modifications
4
Control Modes
Sim • URSim • Hybrid • Production
<5ms
Control Loop
Real-time performance
6-DOF
Motion Planning
+ 1-DOF gripper

## Slide 11
Future Work & Enhancements
👁
Vision-Guided Grasping
• YOLOv8 object detection
• RealSense depth integration
• Pose estimation pipeline
⚡
Force Control
• Force/torque sensing
• Compliant manipulation
• Contact detection
🤖
Multi-Robot Coordination
• ROS_DOMAIN_ID isolation
• Coordinated motions
• Shared workspace
🎯
Advanced Planning
• Dynamic re-planning
• Obstacle avoidance
• Optimization metrics

## Slide 12
Thank You
Questions & Discussion
Repository: github.com/your-repo/my_ur_description Tag: v1.1.8_2f-85 Branch: ur12e_2f-85_action_server